|  | ......................... pcs. .............................. € .............................. € External flashlight for visual alarm indication Sturdy, maintenance-free and fail-safe design, xenon tubes for high visibility performance, one flash is emitted per second. For optional combination with external signal horn, flush-mounted, Polycarbonate housing; Operating voltage 20-30 V DC; Current consumption 90 mA; Protective class IP 54 Dimensions (diameter x height): 93 x 72 mm Reflector colour: red |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € External signal horn for acoustic alarm indication With 26-fold adjustment signal tone, volume control from 74 - 94 dB (A) at distance of 1 m away with 24 V. Operating voltage 10-28 V DC, Current consumption 16 mA Protection rating IP54 Dimensions Surface-mounted:(diameter x height) 111 x 25.5 mm, Flush-mounted: 81 x 81 x 62.5 mm ( ) Surface mounting, white ( ) Flush-mounted installation, switch programme Jung AS 500 alpine white Flush-mounting boxes 62.5 mm deep are required for flush-mounted installation |
|  | ......................... pcs. .............................. € .............................. € SLE 220 external fault indicator lamp for visual state or alarm indication Operating voltage 24 V DC; Current consumption 18 mA; IP rating: IP 20 Surface mounting dimensions (W x H x D) 61 x 61 x 74 mm ( ) Reflector colour: red Flush mounting dimensions (W x H x D) 81 x 81 x 41 mm ( ) Jung AS 500 alpine white, reflector colour: green ( ) Jung AS 500 alpine white, reflector colour: red |
|  | ......................... pcs. .............................. € .............................. € SCT 320 external key switch Flush-mounted unit suitable for switch programme with dimensions of 55 x 55 mm. Including flat ribbon cable for connection to a GEZE TZ 32x door control unit Key switch with 2 switch contacts for switching the functions short-time release, permanent unlocking, locking and for alarm reset Sabotage-proof cover With Euro profile half cylinder Colour: ( ) anthracite ( ) pure white ( ) alpine white Without frame |
|  | ......................... pcs. .............................. € .............................. € SCT 222 external key switch for authorised door passage, Connection to GEZE door control units, Bi-colour LED green/red for indication of the state unlocked / locked, yellow LED for indication of the alarm state Key switch with two-sided switching operation for Unlocking and short-time release/locking Complete with Euro profile cylinder and 3 keys IP rating IP 54 Dimensions (W x H x D): Flush-mounted: Front plate 100x110 mm; flush-mounted box 80x70x45 mm Surface-mounted: 80x70x45 mm ( ) Surface-mounted installation ( ) Flush-mounted installation RP 220 relay board or KL 220 clamping box necessary! |
|  | ......................... pcs. .............................. € .............................. € SCT 221 external key switch For authorised door passage by activating the short-term release function by key for installation on the outside or inside of the door, flush mounting or surface mounting possible without Euro profile half cylinder not permitted on doors with requirements under EN 13637 IP rating: IP 54 Dimensions (W x H x D) Surface-mounted: 75 x 75 x 50 mm Flush-mounted: 75 x 75x 61 mm, 50 mm deep flush-mounted box made of Zamak is included in the scope of supply. ( ) Surface-mounted installation ( ) Flush-mounted installation |
|  | ......................... pcs. .............................. € .............................. € SCT 220 UP external key switch for authorised door passage by activating the short-term release function by key, for installation on the outside or inside of the door, flush-mounted installation Complete with Euro profile cylinder in the single frame IP rating: IP 20 Dimensions (W x H x D): 81 x 81 x 62.5 mm Flush-mounting boxes 62.5 mm deep are required for flush-mounted installation ( ) Jung LS 990 stainless steel ( ) Jung LS 990 alpine white ( ) Gira E2 pure white |
|  | ......................... pcs. .............................. € .............................. € FWS 320 B emergency exit sign Illuminated emergency push-button information label, flush-mounted Flush-mounted unit suitable for 55 x 55 mm switch programme. Integrated illuminated emergency push button information label with LEDs aligned in the same way Operating voltage 24 V DC Current consumption 30 mA Without frame ( ) Design in accordance with EltVTR ( ) Design in accordance with EN 13637 |
|  | ......................... pcs. .............................. € .............................. € FWS 320 emergency exit sign Emergency push button information label, not illuminated, flush-mounted Suitable for 55 x 55 mm switch programme. Integrated emergency push button information label, not illuminated Without frame ( ) Design in accordance with EltVTR |
|  | ......................... pcs. .............................. € .............................. € NOT 320 UP emergency push button Illuminated emergency push button integrated behind the transparent cover for flush-mounted installation, illumination with long-life LED Operating voltage: 24 V DC (+/- 10%) Current consumption: 30 mA IP rating: IP20 Dimensions (W x H x D): 55 x 55 x 27 mm For installation in standard flush-mounted box, depth 46 mm ( ) Jung AS 500 alpine white ( ) Jung LS 990 stainless steel (with intermediate frame) ( ) Jung LS 990 alpine white (with intermediate frame) ( ) Gira E2 pure white For central activation of all door control units via the safety circuit. |
|  | ......................... pcs. .............................. € .............................. € NOT 320 AP emergency push button Illuminated emergency push button with transparent, large flat cover for surface mounting, activated by a button integrated behind the impact cover, illumination with long-life LED Operating voltage: 24 V DC (+/- 10%) Current consumption: 30 mA IP rating: IP20 Dimensions (W x H x D): 55 x 55 x 27 mm ( ) Jung AS500 alpine white ( ) Gira Profil 55 aluminium ( ) Gira Profil 55 white |
|  | ......................... pcs. .............................. € .............................. € NOT 220 UP emergency push button Illuminated emergency push button with lead-sealable reusable cover for flush-mounted installation, complete with single frame and "emergency exit" sign, illumination with long-life LED Operating voltage: 24V DC Current consumption: 17 mA IP rating: IP20 Dimensions (W x H x D): 81 x 81 x 62.5 mm 62.5 mm deep flush-mounted boxes are needed for installation ( ) Gira E2 pure white |
|  | ......................... pcs. .............................. € .............................. € NOT 220 AP emergency push button (plastic) Illuminated emergency push button with lead-sealable reusable cover for surface mounting, complete with "emergency exit" sign, plastic housing, Illumination with long-life LED. Operating voltage: 24 V DC Current consumption: 17 mA IP rating: IP65 Colour: light grey Dimensions (W x H x D): 94 x 94 x 81/122 mm |
|  | ......................... pcs. .............................. € .............................. € Mounting for emergency push button information label Plexiglass with spacers Dimensions (W x H x D): 100 x 100 x 21 mm |
|  | ......................... pcs. .............................. € .............................. € PowerReserve STEP-UPS uninterrupted power supply To maintain the power supply to components of the GEZE escape route protection system and other GEZE door systems in the event of a power failure Properties Compact, low-maintenance and operationally reliable current buffer for top hat rail mounting for use with 24 V DC power supply, Equipment Integrated and long-life lithium-ion battery module, battery module replaceable, Integrated cyclical battery monitoring function, Integrated LED status display, 2 voltage outputs, 3 outputs to communicate the battery mode, charging status and alarm status, Buffer time can be set via rotary switch, Remote function to activate/deactivate the buffer function, Plastic housing; Technical data Rated supply voltage 24 V DC; Input voltage range 22.5 V DC – 29.5 V DC; Rated output voltage 24 V DC; Output voltage range 23 V DC – 26.5 V DC; Current consumption max. 4.7 A; Current consumption (when charging) < 0.5 A; Rated output current (continuous) 3 A; Output current max. 4 A; Capacity 46 Wh; Efficiency 98%; Dimensions (W x H x T) 108 x 90 x 71 mm; Weight 0.5 kg; Ambient temperature (operational) 0 °C – 40 °C; IP rating IP20 |
|  | ......................... pcs. .............................. € .............................. € RP 220 relay board for universal use in connection with TZ 320, for the connection of access control systems, key switch, motors lock and much more. |
|  | ......................... pcs. .............................. € .............................. € Log book for the documentation of acceptance tests and servicing |
|  | ......................... pcs. .............................. € .............................. € Toplock CTS V number codelock, in metal housing, with metal keypad with protection against vandalism, for entering 1 to 6-digit codes, incl. separate evaluating unit, on separate mounting plate Potential-free relay output, impulse 1 s Operating voltage: 230V AC IP rating: IP65 IP rating of the evaluating unit: IP43 Dimensions of the evaluating unit: 188 x 110 x 40 mm (W x H x D) ( ) CTS V (80x80x15 mm WxHxD) ( ) CTS BV with lighting (60x126x23 mm WxHxD) |
|  | ......................... pcs. .............................. € .............................. € GEZE T 320 Terminal for parallel operation and display of TZ 32x door control units for bidirectional protection of an escape and rescue route. Features: • Control unit with illuminated emergency push button LED displays for the following operating states: - Door locked/unlocked/short-term released - Door open/closed - Alarm, pre-alarm, fault Large-surface barrier-free impact cover with sabotage protection. • Integrated emergency push button information label, not illuminated • Operating voltage 24 V DC Version: ( ) Emergency push button information label ( ) Design in accordance with EltVTR ( ) Design in accordance with EN 13637 (note: an additional notice sign is required according to the EltVTR on doors with requirements under EN 13637 and the EltVTR) ( ) Lighting for the integrated emergency push button information label ( ) Key switch with 2 switch contacts incl. Euro profile half cylinder for setting the functions short-time release, permanent unlocking, locking and alarm reset ( ) Surface-mounted installation: Plastic housing, dimensions (W x H x D): 77x197x 90 mm ( ) Colour similar to RAL 6032 (green) ( ) Colour: white aluminium Stainless steel housing Housing, dimensions (W x H x D): 78 x 240 x 68.5 mm Front plate, dimensions (W x H x D): 78 x 240 x 1.5 mm ( ) Stainless steel V2A, brushed ( ) With LED backlight red/green to indicate system statuses by means of backlighting ( ) Flush-mounted installation: Switch programme, dimensions (W x H x D): Triple frame 81 x 223 x 62.5 mm ( ) AS500 in alpine white by Jung ( ) LS990 in stainless steel by Jung ( ) LS990 in alpine white by Jung ( ) E2 in pure white by Gira ( ) E2 in anthracite by Gira Stainless steel in flush-mounted box Housing, dimensions (W x H x D): 77 x 239 x 68.5 mm Front plate, dimensions (W x H x D): 98 x 260 x 1.5 mm ( ) Stainless steel, brushed ( ) With LED backlight red/green to indicate system statuses by means of backlighting Stainless steel in flush-mounted boxes Front plate, dimensions (W x H x D): 98 x 260 x 1.5 mm Spacer frame, dimensions (W x H x D): 98 x 260 x 10 mm Installation of the individual components (control unit, key switch) in deep standard flush-mounted boxes ( ) Front plate in brushed stainless steel, acrylic white spacer frame ( ) With LED backlight red/green to indicate system statuses by means of backlighting |
|  | ......................... pcs. .............................. € .............................. € CAN Ethernet gateway Ethernet connection of automatic doors or escape route terminals via a manufacturer-specific CAN-bus (up to two CAN lines) to a building automation controller. Contains a specific configuration file. Dimensions: 70 x 100 x 61 mm (W x H x D) Ambient temperature 0 °C to +70 °C Power supply 24 V DC IP rating: IP20 |
|  | ......................... pcs. .............................. € .............................. € BUS repeater for extending a manufacturer-specific CAN-bus line by a further 900 m for installation on standard carrier rails Operating voltage: 10 – 32V DC Current consumption: 80 mA (at 24 V DC) Dimensions (W x H x D): 35.2 x 66 x 102.6 mm IP rating: IP20 Several repeaters and carrier rail connectors are needed for implementing star and tree structures. |
|  | ......................... pcs. .............................. € .............................. € Housing Surface mounted housing with top-hat rail for holding up to 5 repeaters and power supply. Dimensions (W x H x D): 300 x 150 x 120 mm |
|  | ......................... pcs. .............................. € .............................. € Carrier rail connector for carrier rail power supply, gold-plated contacts, for mounting on carrier rail, 5-pole. For the connection between repeaters. |
|  | ......................... pcs. .............................. € .............................. € NET 320 power supply For installation in flush-mounted box Plastic housing, cast module Input voltage: 230 V AC, 50 Hz Output voltage: 24 V DC (+/- 5 %) Output current: 750 mA, 18W Dimensions: 55.7 x 33 mm (dia.xD) |
|  | ......................... pcs. .............................. € .............................. € NT 19.2-24 power supply For wall installation in plastic housing Input voltage: 230 V AC Output voltage: Power supply 24 V DC Output current: 800 mA, 19.2 W IP rating: IP 54 Dimensions: 100 x 32 x 32 mm (W x H x D) |
|  | ......................... pcs. .............................. € .............................. € NT 1.1 A-24 V UP power supply Input voltage: 230 V AC Power: 26.4 W Output voltage: 24 V DC ± 5% Output current: 1.1 A Version: For installation in deep standard flush-mounted boxes |
|  | ......................... pcs. .............................. € .............................. € POWER SUPPLY NT 1.5 A-24V HS Technical data: Input voltage: 230 V AC Power: 36 W Output voltage: 21.6 - 26.4 V DC ±1%, adjustable Output current: 1.5A Version: Top hat rail housing, 2 division units Dimensions W x H x D [mm]: 35 x 90 x 58 |
|  | ......................... pcs. .............................. € .............................. € POWER SUPPLY NT 2.5 A-24V HS Technical data: Input voltage: 230 V AC Power: 60 W Output voltage: 21.6 - 26.4 V DC ±1%, adjustable Output current: 2.5A Version: Top hat rail housing, 3 division units Dimensions W x H x D [mm]: 52 x 90 x 58 |
|  | ......................... pcs. .............................. € .............................. € Power supply NT 6.25 A-24 V HS Technical data: Input voltage: 230 V AC +/-10 % Power: 150 W Output voltage: 24 V DC +-3% (SELV) Output current: 6.25 A Version: Top hat rail housing, 4 division units Dimensions (W x H x D): 72 x 95 x 66.5 mm |