|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 5000, for installation on fire and smoke protection doors, with infinitely adjustable closing force size 2 – 6 in accordance with EN 1154,with guide rail; closing force, closing speed, back check and latching action are front adjustable, with visual closing force display, standard installation on door leaf/hinge side, with mounting plate Alternative to the guide rail: ( ) with T-Stop guide rail, with integrated opening restrictor Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) stainless steel optic ( ) acc. to RAL |
| --- | --- |