|  | ......................... pcs. .............................. € .............................. € Integrated door closer system GEZE Boxer ISM-EFS 24 V DC, for 2-leaf single-action doors from 50 mm door leaf thickness, adjustable closing force size 4-6 in accordance with EN 1154, guide rail with integrated mechanical closing sequence control in accordance with EN 1158, with free swing function on the active leaf, activated through electric hold-open device by opening the door once to approx. 90°, in accordance with EN 1155, with comfort hold-open function for light holding in place at the maximum opening angle of the free swing area to prevent the door from closing unintentionally. Vandalism protection against wilful maloperation of the closing sequence control Closing speed and latching action can be adjusted after installation. The closers are completely installed inside the door leaf, the guide rail can only be seen when the door is open. Up to 180 kg door leaf weight / door width 1400 mm for left and right single-action doors Barrier-free in accordance with DIN 18040 When used on fire and smoke protection doors, a suitability certificate is required for the door. Hinge distance: min.: 1300 mm max.: 2800 mm Colour: ( ) silver-coloured Accessories: ( ) Integrated, almost invisible flexible opening restrictor for E/R/ISM guide rails GEZE current interruption switch (compulsory for free swing door openers) ( ) Surface-mounted ( ) Flush-mounted Note: Please note the general building approval from DIBt (German Centre of Competence for Construction). |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE RSZ 7 smoke switch control unit, suitable for installation on fire and smoke protection closers, extendable, with telescopic function, for bridging unfavourable lintel situations, 30 mm overall height, in GEZE design, with adaption of the alarm threshold, contamination indicator and integrated test button, integrated line monitoring to ceiling-mounted detector and manual trigger switch, for connection of GEZE hold-open devices, approved by DIBt as hold-open system for fire protection closers, EN 14637 compliant Connection: 230V AC Output voltage: 24 V DC, 250 mA For lintel height > 1 m, 2 additional ceiling-mounted detectors are needed. Colour: ( ) silver-coloured ( ) white ( ) stainless steel effect ( ) RAL ….. |
|  | ......................... Pcs. .............................. € .............................. € GEZE FA GC 170 wireless extension for connecting wireless components to GEZE hold-open systems without cables, consisting of: GEZE GC 171 wireless module for connection to GEZE hold-open systems, 24 VDC supply directly via GEZE hold-open system, set up with dip switch without additional programming tools, display of connection quality and status for every device, encrypted wireless connection, wireless integration of up to six devices GC 172 / GC 173 / GC 175 tested in accordance with EN 54-25 and EN 54-18, general type approval for GEZE hold-open systems ( ) GEZE GC 172 wireless ceiling-mounted smoke detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-7 and EN 54-25, with adaption of the alarm threshold in accordance with DIN14677, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 173 wireless ceiling-mounted thermal detector, complete with base, for wireless connection to the GEZE GC171 wireless module, encrypted wireless connection, battery-operated, battery life 8 years, tested in accordance with EN 54-5 and EN 54-25, EN 14637 compliant, general type approval for GEZE hold-open systems ( ) GEZE GC 175 wireless input module for wireless connection to the GEZE GC 171 wireless module, connection to manual trigger switch or potential-free contact of a fire alarm system, encrypted wireless connection, battery operated, battery life 5 years, tested in accordance with EN 54-25 and EN 54-18, installed in flush mounted socket EN 14637 compliant, general type approval for GEZE hold-open systems |
|  | ......................... pcs. .............................. € .............................. € GEZE smoke detector GC 152, 24 V, complete with base, tested in accordance with EN 54-7, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE thermal detector GC 153, 24 V, complete with base, tested in accordance with EN 54-5, integrated line monitoring, conform with DIN EN 14637, can be connected to smoke switch control unit (2 pcs.) Colour: ( ) white ( ) RAL … |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is with variable adjustment (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |
|  | ......................... pcs. .............................. € .............................. € Acceptance test for the hold-open system and permanent attachment of the sign of approval |
|  | ......................... pcs. .............................. € .............................. € GEZE hold-open magnets Operating voltage 24 V DC Power consumption 1.5 W Retention force 490 N ( ) Hold-open magnet basic model (zinc plated without base plate) for in-wall installation or installation in any construction ( ) Hold-open magnet for wall mounting with base plate ( ) Hold-open magnet for flush-mounted installation ( ) Hold-open magnet for surface installation ( ) Base for hold-open magnet surface-mounted for floor installation ( ) Hold-open magnet with spacer tube zinc plated for floor/ceiling/wall mounting with swivelling magnetic head ( ) Version in basic length 185 mm ( ) Version in basic length 335 mm ( ) Hold-open magnet for wall mounting, basic length 65 mm GEZE magnetic counter plates, ( ) Standard magnetic counter plate on mounting plate with spring system for flatness with hold-open magnet ( ) Magnetic counter plate with spring buffer on installation housing with damping spring for soft spring buffer for heavy doors ( ) Magnetic counter plate, swivelling on mounting plate with swivelling magnetic counter plate for angle positions between door and hold-open magnet |
|  | ......................... pcs. .............................. € .............................. € GEZE current interruption switch for manual triggering ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (standard) Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Maintenance and testing of hold-open systems (optional position) with warranty extension Service package for maintenance and testing according to DIBt approval and according to manufacturer’s specification, with the following features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months at the latest after the commissioning date) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - No separate charging for consumables up to EUR 25 per maintenance service - No separate charging for working hours when spare parts are replaced during the maintenance - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without additional costs (exceptions: Sundays and national holidays) - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |